## Slide 1: Fluids Review
Head loss, shear, vena contracta, and other concepts that enable a “smart fluids” design

## Slide 2: Motivation
We will use smart physics and fluids to create elegant designs
Computer controlled flows and water levels in water treatment plants are
  a lazy approach to design
  prone to failures (not a resilient design approach)

## Slide 3
Dominant Design Constraint?
Notes: What was the constraint used to create this design???? Constraints matter! The design you create will strongly reflect the constraints that you used to guide the design.

## Slide 5: Fluids Review
Drag (flow around objects)
Head loss (flow in pipes and channels)
Bernoulli and Energy Equation

## Slide 6
Pressure drag (normal force)
Shear drag (tangent force)
Lift drag
What causes the majority of air drag on a bicycle (including the rider)?

## Slide 7: drag
Round disk tangent to wind
Round disk perpendicular to wind
Hemisphere with convex side facing wind
Hemisphere with concave side facing wind
Which orientation causes more drag?

## Slide 8: Streamlines
Draw the streamlines that begin on the upstream side of the object for these two cases
Which object has the larger wake?
Which object has the lower pressure in the wake? (if streamlines are bending hard at the point of separation, then the streamlines will be close together…)

## Slide 9: Why is there drag?
Fluid separates from solid body and forms a recirculation zone
Pressure in the recirculation zone must be low because velocity in the adjacent flowing fluid at the point of separation is high
Pressure in recirculation zone (the wake) is relatively constant because velocities in recirculation zone are low
Pressure behind object is low - DRAG

## Slide 10: luggagebehindortop
on the roof rack on top of the car.
on the hitch behind the car.
I’m going on vacation and I can’t pack all of our luggage in my car. Where should I put it to reduce the drag on the car?

## Slide 11: BernoulliOrEnergy
Control Volume Energy equation
Bernoulli equation
These are the same equations
Which equation do you use to measure the head loss in a pipe system?

## Slide 12: InefficientConversion
Potential energy (pressure or elevation) converted to kinetic energy in an abrupt flow contraction
Kinetic energy converted to potential energy in an abrupt flow expansion
Note: This is the same as asking, “Where can you apply the Bernoulli equation?”
Which conversion loses mechanical energy to heat?
Notes: Acceleration is efficient!!!!
Deceleration is inefficient!
Where can you apply Bernoulli?

## Slide 13: Orifice Equation
Bernoulli equation (no energy loss)
Orifice Equation (memorize this!)
z1
z2 = 0
mechanical
^
Flow contraction!
Area of the constricted flow
Continuity equation

## Slide 14: Orifice Equation
This equation applies to a horizontal orifice (so that the depth of submergence is constant throughout the entire orifice area). For depth of submergence larger than the diameter of the orifice this equation can be applied to vertical orifices. There is a general equation for vertical orifices in physchem.py within aguaclara.
z1
z2 = 0
Flow contraction!

## Slide 15: Two kinds of drag Two kinds of head loss
Drag (external flows)
Skin (or shear) friction
  Shear on solid surface
  Classic example is flat plate
Form (or pressure) drag
  Separation of streamlines from solid surface and wake results in a…
  Flow expansion (behind object)
Head loss (internal flows)
Major losses (hf – friction)
  Shear on solid surface
  Shear on pipe walls
Minor losses (he – expansion)
  Separation of streamlines from solid surface results in a…
  Flow expansion
Energy equation (NOT THE BERNOULLI EQUATION)

## Slide 16
They both have significant energy losses due to shear between fluid and the solid surface
They both have significant energy losses due to flow expansions
A long streamlined train and a long straight pipeline are similar in that

## Slide 17: Head Loss in a Long STRAIGHT Tube (due to wall shear): Major Losses
Darcy Weisbach:
Transition from turbulent to laminar occurs at Re~2100
This equation gives the major losses for BOTH laminar and turbulent flow.
How to find the friction factor for wall shear, f?
First, find Reynold’s number

## Slide 18: Head Loss in a Long STRAIGHT Tube (due to wall shear): Major Losses
Laminar
if Re < 2100,
Swamee-Jain:
Turbulent
if Re > 2100,
hf proportional flow
Where Ɛ is the wall roughness
Hagen-Poiseuille:
Major loss equation simplification
(for laminar flow only!):
(no hf equation simplification😢)

## Slide 19: Frictional Losses in Straight Pipes: Moody Diagram
0.01
0.1
1E+03
1E+04
1E+05
1E+06
1E+07
1E+08
Re
friction factor
laminar
0.04
0.03
0.02
0.015
0.01
0.008
0.006
0.004
0.002
0.001
0.0008
0.0004
0.0002
0.0001
0.00005
smooth
0.05

## Slide 20: TurbulentHeadLoss
Decreases with increased flow
Remains constant with increased flow
Increases approximately in proportion to the flow
Increases approximately in proportion to the square of the flow
Increases in proportion to the natural log of the flow
Head loss through a long, rough pipe with turbulent flow

## Slide 21: Head Loss: Minor Losses
Head (or energy) loss (hL) due to: outlets, inlets, bends, elbows, valves, pipe size changes
Losses are due to expansions
Losses can be minimized by gradual expansions
Minor Losses have the form where Ke is the loss coefficient and V is some characteristic velocity (could be contracted flow or expanded flow)
When V, KE  thermal

## Slide 22: Three forms of Minor Loss equation
Most commonly used form
in
out
Vin
Vout
Notes: Emphasize the minor loss coefficient is defined based on some relevant velocity. We can chose either V1 or V2. But the magnitude of the minor loss coefficient is determined by which velocity we use. We need to choose one and be consistent. The velocity that we choose will be a function of convenience. Minor losses are proportional to the square of the velocity. This is true whether the flow is turbulent or laminar!

## Slide 23: Which points are `in` and `out` for finding the Minor Loss coefficient?
`in` should be where the flow is most compressed
`out` should be where the flow has fully expanded
B
A
C
Notes: Draw the orifice case in detail showing expansion zone

## Slide 24: Three forms of Minor Loss equation
out
Vout
Vin
Most commonly used form
Which form of velocity is easier to measure, Vin or Vout?
Which form of K can be greater than 1, Ke or Ke’?
What does it mean when Ke exceeds 1?
What is the Ke for a pipe discharging into a lake?
1
in
Notes: Emphasize the minor loss coefficient is defined based on some relevant velocity. We can chose either V1 or V2. But the magnitude of the minor loss coefficient is determined by which velocity we use. We need to choose one and be consistent. The velocity that we choose will be a function of convenience. Minor losses are proportional to the square of the velocity. This is true whether the flow is turbulent or laminar!

## Slide 25: MajorMinorDrain
major losses dominate
minor losses dominate
minor losses are equal to major losses
When draining a tank through a valve

## Slide 26: Elevation difference = head loss trick
Small diameter tubing
Also called the ‘head loss trick’ or ‘control volume trick
This trick is used extensively in this class,
understanding it will make it easier to understand
future course concepts!
Notes: Draw the orifice case in detail showing expansion zone

## Slide 27: Elevation difference = head loss trick
Small diameter tubing
Also called the ‘head loss trick’ or ‘control volume trick
The kinetic energy term gets incorporated in head loss as a minor loss with a Ke of 1
Click here for a more in-depth explanation
Notes: Draw the orifice case in detail showing expansion zone

## Slide 28: VerticalPipe
AguaClara/PRADAN Solar Pumped System in Jharkhand India
Transmission Line Length
Minimum height for adequate pressure at highest tap
Solar panels
Pump control room
Water treatment facility
Maximum elevation change
Minimum well water level

## Slide 29
2.5 cm diameter
5 cm diameter
7.5 cm diameter
10 cm diameter
What size pipe should be used for the vertical section up the tank to maximize flow?
A 10 cm diameter pipe is used for the 500 m long transmission line
The elevated tank is 10 m tall.
What are the failure modes?
What are the constraints?

## Slide 30: How can you make water flow up through a tank (by gravity)?