## Slide 1: The State of the Planet
Sustainable Development Goals

## Slide 2: Class Logistics
Learn python!
Post issues at https://github.com/AguaClara/CEE4520/issues

## Slide 3
a sage on the stage
a guide by my side
Cornell Professors are

## Slide 4
How do we make the most out of lectures?

## Slide 5: Overview
Burden of unsafe water
The Sustainable Development Goals
  Safe and Improved…
Intermittent Supplies
The technology is well developed…
  Cell phones vs. municipal water technology
A role for universities
Ctrl + click the pictures to go each section!

## Slide 6: Overview
Ctrl + click the pictures to go each section!
Burden of unsafe water
The Sustainable Development Goals
  Safe and Improved…
Intermittent Supplies
The technology is well developed…
  Cell phones vs. municipal water technology
A role for universities

## Slide 7: WHO Fact sheet on water (2017): The good news
“In 2015, 71% of the global population (5.2 billion people) used a safely managed drinking-water service – located on premises, available when needed, and free from contamination.”
But let’s bring skepticism to this statement
This conclusion was made without collecting data on water quality in rural areas
(World Health Organization)
Notes: http://www.who.int/mediacentre/factsheets/fs391/en/
https://www.ircwash.org/blog/third-glass-three-quarters-full?utm_source=Amplify&utm_campaign=5c4000cc1e-Amplify_Aug_2017&utm_medium=email&utm_term=0_d60e6862b4-5c4000cc1e-48437621
Honduran government doesn’t even know how to contact the vast majority of the community water providers!

## Slide 8: UN Fact sheet on water (2017) The bad news
884 million people lack even a basic drinking-water service, including 159 million people who are dependent on surface water
Globally, at least 2 billion people use a drinking water source contaminated with feces
Contaminated water can transmit diseases such diarrhea, cholera, dysentery, typhoid, and polio
Contaminated drinking water is estimated to cause 502,000 diarrheal deaths each year
Notes: http://www.who.int/mediacentre/factsheets/fs391/en/
Rediculous number of significant digits. This is 1 billion and it might be 3 people…
This suggests that for a basic service it is okay if it contains feces.

## Slide 9: UN Fact sheet on water (2015)
By 2025, half of the world’s population will be living in water-stressed areas
In low- and middle-income countries, 38% of health care facilities lack any water source, 19% do not have improved sanitation and 35% lack water and soap for handwashing
Notes: http://www.who.int/mediacentre/factsheets/fs391/en/

## Slide 10: Safe Tap Water According to the CDC
A Traveler's Guide to Tap Water
September 10, 2014 by Danny Ashton
Notes: A Traveler's Guide to Tap Water
September 10, 2014 by Danny Ashton
http://lifehacker.com/know-what-countries-guarantee-drinkable-tap-water-with-1635070463

## Slide 11: Which problems are we solving?
Majority World problems?
  The world lacking basic infrastructure (includes parts of Tompkins county)
Minority World problems?
  The world focused on self driving cars, smart cities, and Amazon Prime
A modest proposal: I will focus most of my creative energies on solving problems for the Majority World.

## Slide 12: Honduras Stats as of 2015 (from WHO)
Population with sustainable access to an improved water source
  Urban – 97.4%
  Rural – 83.8%
See extra 1
Notes: http://apps.who.int/gho/data/node.main.46?lang=en

## Slide 13: Cost vs required personal effort: Current paradigm myth!
Per-capita cost
Personal (or household) effort required
Centralized water treatment
Vended water
Ceramic filters
Boiling
POU chlorination
Solar Disinfection
What are the assumptions underlying this infographic?
Notes: Adapted from presentation by Amy Pickering at Cornell University in December 2018.
Cost of centralized water treatment is the treatment part! This forgets that in a city you need centralized water provision in any case.
Vended water means tanker trucks instead of a distribution pipe network!!!!! Are we really saying tanker truck water is cheaper than piped water????
If you don’t have a water supply system that you don’t have any water to boil.
Boiling doesn’t make water that is aesthetically pleasing.
This forgot to ask what the consumer wanted!
Check the math!

## Slide 14: Value of Service and Willingness to Pay
Cost of service ($/month)
Willingness to Pay ($/month)
Economics background: cost/quality framework
  How do we understand the failure of some systems?
  Where is the “sweet spot” for sustainability?
Untreated river water at the tap
Traditional Mechanized plant
AguaClara plant
Service method
Break-even line
Minimum quality for public health
2
1
3
Notes: The cases of 1 (small towns less than 25,000) and 2 (towns larger than 25,000) in Honduras are the norm.

## Slide 15: Overview
Ctrl + click the pictures to go each section!
Burden of unsafe water
The Sustainable Development Goals
  Safe and Improved…
Intermittent Supplies
The technology is well developed…
  Cell phones vs. municipal water technology
A role for universities

## Slide 16
2015 to 2030
Notes: On 1 January 2016, the 17 Sustainable Development Goals (SDGs) of the 2030 Agenda for Sustainable Development — adopted by world leaders in September 2015 at an historic UN Summit — officially came into force. Over the next fifteen years, with these new Goals that universally apply to all, countries will mobilize efforts to end all forms of poverty, fight inequalities and tackle climate change, while ensuring that no one is left behind.
http://www.un.org/sustainabledevelopment/development-agenda/

## Slide 17: United Nations
“By 2030, achieve universal and equitable access to safe and affordable drinking water for all”
“Support and strengthen the participation of local communities in improving water and sanitation management” http://www.un.org/sustainabledevelopment/water-and-sanitation/

## Slide 18: SDG 6.1: By 2030,safe and affordable drinking water for all
Some three in ten people (2.3 billion) lack access to safe and readily available water at home (or maybe it is 5 in 10…)
Additional 1.2 billion from population growth gives 3.5 billion need water by 2030
  267 million people per year!
  800,000 L/s per year of new installed capacity
  Water for 18 New York Cities per year!
Notes: http://www.un.org/sustainabledevelopment/blog/2017/07/billions-around-the-world-lack-safe-water-proper-sanitation-facilities-reveals-un-rep
Assumes 3 mL/s
NYC is 1 BGD = 44000 L/s
18 NYC per year

## Slide 19: We forgot to include replacement of failing plants
Notes: La Esperanza, Honduras

## Slide 20: 4.9 billion need new water supply systems by 2030
48 year lifetime
12 years until 2030
25% of existing plants need to be replaced
Supposedly 5.6 billion have safe water on tap
1.4 billion need upgraded systems by 2030

## Slide 21: Overview
Ctrl + click the pictures to go each section!
Burden of unsafe water
The Sustainable Development Goals
  Safe and Improved…
Intermittent Supplies
The technology is well developed…
  Cell phones vs. municipal water technology
A role for universities

## Slide 22: Intermittent Supplies
It is estimated that over one-third of the urban water supplies in Africa, and in Latin America and the Caribbean, and more than half those in Asia, operate intermittently.
Why are supplies intermittent? _______________
  Crude form of rationing
  Lack of meters
  Leaking system – reduce amount of water lost
  Some sections of the city might never receive water otherwise
  Elevation challenges!
Rolling blackouts
Notes: http://www.who.int/docstore/water_sanitation_health/Globassessment/Global3.4.htm

## Slide 23
I’ve always had accessed to water at the tap
I visited a city where water was intermittent
I grew up in a town or city where water was intermittent
What is your experience with intermittent water supply?

## Slide 24: You just acquired a hotel in downtown Delhi, India
Electricity is intermittent, what do you do?
Water is intermittent, what do you do?
  How can you get more water?
  How does each affect your water quality?

## Slide 25: Leaks don’t cause contamination unless the flow is INTO the pipe
Necessary conditions:
  Saturated contaminated soil
  Leaky Pipe
  Pressure outside pipe must exceed pressure inside pipe
Potential Causes:
  Negative pressure transients
  Booster pumps
*Photo credits
Top: http://texas-slab-leak-repair.com/water_leak
Bottom: Emily Kumple
Notes: David Gold, Alicia Peters, Weier Chen,Lucia Garcia-Iturri Gallego, Distribution System Contamination Prevention
https://docs.google.com/presentation/d/1FbHpETKLk-6JZaqnlvxxkkQqu3iSUCvia9jvmYfr5kg/edit#slide=id.p21

## Slide 26: Booster pumps that pull water from the distribution system should be banned
Image credits: http://www.egr.msu.edu/~fultras-web/images/applications/gui/PressureWaveform.png
Emily Kumple
Pressure Transients
Boster Pumps
Notes: David Gold, Alicia Peters, Weier Chen,Lucia Garcia-Iturri Gallego, Distribution System Contamination Prevention
https://docs.google.com/presentation/d/1FbHpETKLk-6JZaqnlvxxkkQqu3iSUCvia9jvmYfr5kg/edit#slide=id.p16

## Slide 27: The Point of Use (POU) Treatment Option
A Hypothesis – Given that
  centralized water supply systems always have leaks
  intermittency is common when water is in short supply
  contaminated water can flow into the supply pipes when they aren’t pressurized
  Centralized systems often fail to meet standards
Household level (Point of Use) is the best option for drinking water treatment
Notes: Discuss and then vote

## Slide 28: Overview
Ctrl + click the pictures to go each section!
Burden of unsafe water
The Sustainable Development
Goals
  Safe and Improved…
Intermittent Supplies
The technology is well developed…
  Cell phones vs. municipal water technology
A role for universities

## Slide 29: Technology isn’t the problem
Former World Health Organization Director-General: Dr Gro Harlem Brundtland speech at Cornell University in 2005
Loosely paraphrasing…
We have the technology to solve the world’s problems – what is missing is education, institutional capacity, and political will
Notes: This is the “engineers are irrelevant hypothesis”.

## Slide 30
AND
Policy, Education, Institutions
Technologies

## Slide 31: Policy, Education, Institutions or Engineering
You can sometimes compensate for poor engineering by providing more inputs
  Energy – fossil fuels
  Education
  Money
  Management
  Labor
You can sometimes reduce this burden on society by improving the technologies
These factors are multipliers!!!!
and

## Slide 32: Multipliers
1x1x1x1x1x0=0
  Energy x Education x Money x Governance x Labor x Technology = ?
1x1x½x1x1x2=1

## Slide 33: Suppose distillation were the only method that environmental engineers had developed to create clean water
All water in pipes delivered to homes was unsafe
What would you say is the limiting factor preventing implementation of safe piped water?
  Weak institutions
  Corruption
  Weak Economies
  Poor education
  Inadequate technology
What do you conclude?
Notes: We have the technology. The problem is weak economies.

## Slide 34: Why aren’t there better technology choices?
We have a solution that works for strong economies (conventional water treatment)
Individual cities can’t afford to hire consulting firms to conduct research to develop better technologies
Each city chooses conservative existing designs
The same is true for countries in the Majority World (they can’t afford the R&D to develop better technologies)

## Slide 35: Continual optimization? Cell Phones vs. Water Treatment
Why are cell phones continually getting cheaper and better?
Why is conventional water treatment not enjoying a similar optimization?
  Vendors, Consultants, Municipalities
  What does each entity strive to obtain?

## Slide 36: Cell Phones vs. Municipal Water Treatment
Global! | Cell phones | Municipal Water
Units per year | 850,000,000 | 
Companies | 10? | 100s?
Incentive | Improve technology & increase market share | Successful operation at handover of each customized plant
http://www.industry.siemens.com/Water/en/markets/p_02.htm

## Slide 37: Why has the Private Sector Failed to Optimize Municipal Water Treatment?
Research and development is expensive
Low volume of units and customized designs for each site
Long life of units (at least ideally!)
Vendors want to sell hardware
Consultants want to minimize liability for design
Consultants use vendors to create their designs
Vendor designs don’t need to be patented to maintain market
Can’t risk failure on a unit – conservative design prevails
Ineffective feedback mechanism
Notes: R&D is expensive

## Slide 38: Package Plants

## Slide 39
Dominant Design Constraint?
Notes: What was the constraint used to create this design???? Constraints matter! The design you create will strongly reflect the constraints that you used to guide the design.

## Slide 41: Failure to design for the Operator

## Slide 42: Failure to design for the Operator

## Slide 43: Failure to design for the Operator

## Slide 45: Both “advanced” and “appropriate” technologies can fail
El Progreso,
  Modular BEKOX
  Vulnerable
Siguatepeque
  Civil Work
  Vulnerable
Marcala, Honduras
  No chemicals
  Upflow filtration
  Abandoned (Replaced with AguaClara)
4 veces mas cara que AguaClara
Notes: Ethics of Engineering Experimentation

## Slide 46: Overview
Ctrl + click the pictures to go each section!
Burden of unsafe water
The Sustainable Development Goals
  Safe and Improved…
Intermittent Supplies
The technology is well developed…
  Cell phones vs. municipal water technology
A role for universities

## Slide 47: A Role for Universities
Develop new knowledge
Test the designs in full scale field trials
Make that knowledge available to the global community
Open source engineering!
Capacity building: training the trainers
Bring the power of automation to engineering design (Take Henry Ford’s idea out of the realm of widgets and into the realm of knowledge)

## Slide 48: Open-Source University-based Research and Development
Design Studio
Sustainable Infrastructure
New Theories
Research Laboratory
Safe water on tap
Journey Inward
Journey Outward
Notes: From the research lab to new understanding of the physics to the design studio to the construction site to the tap
"research invent design empower"

## Slide 49: Low Carbon Footprint Technologies
Previous generations of engineers designed infrastructure that required cheap fossil fuel
It is long past time for a new paradigm
The original motivation for developing energy efficient technologies was the majority world, but many of these technologies will be the preferred option for wealthier communities too
Everyone likes cheaper, better, and more reliable

## Slide 50: Hypotheses: The Grand Experiment
Technology should be designed based on the conditions under which it will operate
For infrastructure it is more efficient to disseminate knowledge than hardware
We can achieve higher coverage using a model of technology dissemination in which we share knowledge openly

## Slide 51: Where are we going?
Control and measure flow
Rapid Mix
Flocculation
Sedimentation
Disinfection
Filtration
The Challenge!

## Slide 52: State of the Planet
Burden of unsafe water
Intermittent Supplies
extras
Extra 2
Extra 1

## Slide 53: What are extras?
extras are the solution for when there’s just too much exciting information for one presentation!
While fun and exciting, this information will not be on any Design Challenges or exams