## Slide 1: Open Channel Flow

## Slide 2: Open Channel Flow
depth
Liquid (water) flow with a ____ ________ (interface between water and air)
relevant for
  natural channels: rivers, streams
  engineered channels: canals, sewer lines or culverts (partially full), storm drains
of interest to hydraulic engineers
  location of free surface
  velocity distribution
  discharge - stage (______) relationships
  optimal channel design
free surface

## Slide 3: Topics in Open Channel Flow
Uniform Flow
  Discharge-Depth relationships
Channel transitions
  Control structures (sluice gates, weirs…)
  Rapid changes in bottom elevation or cross section
Critical, Subcritical and Supercritical Flow
Hydraulic Jump
Gradually Varied Flow
  Classification of flows
  Surface profiles
normal depth

## Slide 4: Classification of Flows
Steady and Unsteady
  Steady: velocity at a given point does not change with time
Uniform, Gradually Varied, and Rapidly Varied
  Uniform: velocity at a given time does not change within a given length of a channel
  Gradually varied: gradual changes in velocity with distance
Laminar and Turbulent
  Laminar: flow appears to be as a movement of thin layers on top of each other
  Turbulent: packets of liquid move in irregular paths
(Temporal)
(Spatial)

## Slide 5: Momentum and Energy Equations
Conservation of Energy
  “losses” due to conversion of turbulence to heat
  useful when energy losses are known or small
    ____________
  Must account for losses if applied over long distances
    _______________________________________________
Conservation of Momentum
  “losses” due to shear at the boundaries
  useful when energy losses are unknown
    ____________
Contractions
Expansion
We need an equation for losses

## Slide 6: Open Channel Flow: Discharge/Depth Relationship
Given a long channel of constant slope and cross section find the relationship between discharge and depth
Assume
  Steady Uniform Flow - ___ _____________
  prismatic channel (no change in _________ with distance)
Use Energy, Momentum, Empirical or Dimensional Analysis?
What controls depth given a discharge?
Why doesn’t the flow accelerate?
P
no acceleration
geometry
Force balance
A
Compare with pipe flow
What does momentum give us?
What did energy equation give us?
What did dimensional analysis give us?

## Slide 7: Steady-Uniform Flow: Force Balance

W

W sin 
Dx
a
b
c
d
Shear force
Energy grade line
Hydraulic grade line
Shear force =________
W cos 
Wetted perimeter = __
Gravitational force = ________
Hydraulic radius
Relationship between shear and velocity? ___________
toP D x
P
gA Dx sinq
Turbulence

## Slide 8: Open Conduits: Dimensional Analysis
Geometric parameters
  ___________________
  ___________________
  ___________________
Write the functional relationship
Does Fr affect shear? _________
Hydraulic radius (Rh)
Channel length (l)
Roughness (e)
No!

## Slide 9: Pressure Coefficient for Open Channel Flow?
Pressure Coefficient
Head loss coefficient
Friction slope coefficient
(Energy Loss Coefficient)
Friction slope
Slope of EGL

## Slide 10: Dimensional Analysis
Head loss  length of channel
(like f in Darcy-Weisbach)

## Slide 11: Chezy Equation (1768)
Introduced by the French engineer Antoine Chezy in 1768 while designing a canal for the water-supply system of Paris
where C = Chezy coefficient
where 60 is for rough and 150 is for smooth
also a function of R (like f in Darcy-Weisbach)
compare
For a pipe

## Slide 12: Darcy-Weisbach Equation (1840)
where d84 = rock size larger than 84% of the rocks in a random sample
For rock-bedded streams
f = Darcy-Weisbach friction factor
Similar to Colebrook

## Slide 13: Manning Equation (1891)
Most popular in U.S. for open channels
(English system)
very sensitive to n
Dimensions of n?
Is n only a function of roughness?
(MKS units!)
NO!
T /L1/3
Bottom slope

## Slide 14: Values of Manning n
d = median size of bed material
n = f(surface roughness, channel irregularity, stage...)
d in ft
d in m

## Slide 15: Trapezoidal Channel
Derive P = f(y) and A = f(y) for a trapezoidal channel
How would you obtain y = f(Q)?
z
1
b
y
Use Solver!

## Slide 16: Flow in Round Conduits

y
T
A
r
radians
Maximum discharge when y = ______
0.938d

## Slide 17: Velocity Distribution
Chart: v(y) [m/s]
| -1.0271385421279735 | -7.3287282628546058E-2 | 0.8805639768708825 | 1.8344152363703103 | 2.2895179461186097 | 2.7882664958697383 | 3.2433692056180385 | 3.7421177553691689 | 4.0292555958803673 | 4.3163934363915581 | 4.484358305628664 | 4.5482155852372639 | 4.6035312769027472 | 4.6523231748657619 | 4.6959690148685951 | 4.7354514797408314 | 4.7714961461398584 | 4.8046540249780545 | 4.8353534257484592 | 4.8639338841056965 | 4.8906691174139514 | 4.9157830087755459 | 4.9394610153769625 | 4.9618584882274517 | 4.9831068553797895
y | 1e-06 | 1e-05 | 0.0001 | 0.001 | 0.003 | 0.01 | 0.03 | 0.1 | 0.2 | 0.4 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2
0.4d | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
0.2d | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
0.8d | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6
V | 0 | 2
At what elevation does the velocity equal the average velocity?
For channels wider than 10d
Von Kármán constant
V = average velocity
d = channel depth
0.368d
0.4d
0.8d
0.2d
V

## Slide 18: Open Channel Flow: Energy Relations
______ grade line
_______ grade line
velocity head
Bottom slope (So) not necessarily equal to EGL slope (Sf)
hydraulic
energy

## Slide 19: Energy Relationships
Turbulent flow (  1)
z - measured from horizontal datum
y - depth of flow
Pipe flow
Energy Equation for Open Channel Flow
From diagram on previous slide...

## Slide 20: Specific Energy
The sum of the depth of flow and the velocity head is the specific energy:
If channel bottom is horizontal and no head loss
y - _______ energy
- _______ energy
For a change in bottom elevation
y
potential
kinetic
+ pressure

## Slide 21: Specific Energy
In a channel with constant discharge, Q
where A=f(y)
Consider rectangular channel (A = By) and Q = qB
A
B
y
3 roots (one is negative)
q is the discharge per unit width of channel
How many possible depths given a specific energy? _____
2

## Slide 22: Specific Energy: Sluice Gate
Chart: E
1
2
sluice gate
EGL
y1 and y2 are ___________ depths (same specific energy)
Why not use momentum conservation to find y1?
q = 5.5 m2/s
y2 = 0.45 m
V2 = 12.2 m/s
E2 = 8 m
alternate
Given downstream depth and discharge, find upstream depth.
vena contracta

## Slide 23: Specific Energy: Raise the Sluice Gate
Chart: E
1
2
sluice gate
EGL
as sluice gate is raised y1 approaches y2 and E is minimized: Maximum discharge for given energy.

## Slide 24: Step Up with Subcritical Flow
NO! Calculate depth along step.
Chart: E
Short, smooth step with rise Dy in channel
Dy
Given upstream depth and discharge find y2
Is alternate depth possible? __________________________
Chart: E
Energy conserved

## Slide 25: Max Step Up
Chart: E
Short, smooth step with maximum rise Dy in channel
Dy
What happens if the step is increased further?___________
Chart: E
y1 increases

## Slide 26: Step Up with Supercritical flow
Chart: E
Short, smooth step with rise Dy in channel
Dy
Given upstream depth and discharge find y2
What happened to the water depth?______________________________
Increased! Expansion! Energy Loss
Chart: E

## Slide 27: Critical Flow
P
A
T
dy
y
T=surface width
Find critical depth, yc
Arbitrary cross-section
A=f(y)
dA
Hydraulic Depth
Chart: E
yc
More general definition of Fr

## Slide 28: Flow in Round Conduits

y
T
A
r
radians
Maximum discharge when y = ______
0.938d

## Slide 29
radians
Solve for theta and get 1.958 rad
Critical flow

## Slide 30: Solve Max Flow equation for D

## Slide 31: Critical Flow: Rectangular channel
yc
T
Ac
Only for rectangular channels!
Given the depth we can find the flow!

## Slide 32: Critical Flow Relationships: Rectangular Channels
Froude number
velocity head =
because
force
gravity
force
inertial
0.5 (depth)

## Slide 33: Max flow in a short horizontal channel ending in critical depth
q is flow per unit width
Critical depth is 2/3 of the total energy of the flow
The short channel assumption means we are ignoring major losses.
The assumption is that the velocity is zero (H=E) at the upstream end of the channel

## Slide 34: Max flow in a short horizontal channel given constraint on surface elevation change
V is zero at upstream end
Bottom slope is zero
Include wall shear
H is upstream depth

## Slide 35: Channel geometry given a target H/W ratio

## Slide 36: Critical Depth
Minimum energy for a given q
  Occurs when =___
  When kinetic = potential! ________
  Fr=1
  Fr>1 = ______critical
  Fr<1 = ______critical
Chart: E
0
Super
Sub

## Slide 37: Critical Flow
Characteristics
  Unstable surface
  Series of standing waves
Occurrence
  Broad crested weir (and other weirs)
  Channel Controls (rapid changes in cross-section)
  Over falls
  Changes in channel slope from mild to steep
Used for flow measurements
  ___________________________________________
Unique relationship between depth and discharge
Difficult to measure depth
Chart: E

## Slide 38: Broad-Crested Weir
H
P
yc
E
Cd corrects for using H rather than E.
Broad-crested
weir
E measured from top of weir
Hard to measure yc
yc

## Slide 39: Broad-crested Weir: Example
Calculate the flow and the depth upstream. The channel is 3 m wide. Is H approximately equal to E?
0.5
yc
E
Broad-crested
weir
yc=0.3 m
Solution
How do you find flow?____________________
How do you find H?______________________
Critical flow relation
Energy equation
H

## Slide 40: Hydraulic Jump
Used for energy dissipation
Occurs when flow transitions from supercritical to subcritical
  base of spillway
  Steep slope to mild slope
We would like to know depth of water downstream from jump as well as the location of the jump
Which equation, Energy or Momentum?
Could a hydraulic jump be laminar?

## Slide 41: Hydraulic Jump
y1
y2
L
EGL
hL
Conservation of Momentum

## Slide 42: Hydraulic Jump: Conjugate Depths
Much algebra
For a rectangular channel make the following substitutions
Froude number
valid for slopes < 0.02

## Slide 43: Hydraulic Jump: Energy Loss and Length
No general theoretical solution
Experiments show
Length of jump
Energy Loss
significant energy loss (to turbulence) in jump
algebra
for

## Slide 44: Specific Momentum (M)
Chart: E or M
DE
When is M minimum?
Critical depth!

## Slide 45: Hydraulic Jump Location
Suppose a sluice gate is located in a long channel with a mild slope. Where will the hydraulic jump be located?
Do you know either of the conjugate depths?
2 m
10 cm
S = 0.005
Sluice gate
reservoir
Where are we going…

## Slide 46: Gradually Varied Flow: Find Change in Depth wrt x
Energy equation for non-uniform, steady flow
P
A
T
dy
y
Shrink control volume

## Slide 47: Gradually Varied Flow: Derivative of KE wrt Depth
Change in KE
Change in PE
We are holding Q constant!
The water surface slope is a function of:
bottom slope, friction slope, Froude number
Does V=Q/A?_______________
Is V ┴ A?
If gradually varied!

## Slide 48: Gradually Varied Flow: Governing equation
Governing equation for gradually varied flow
Gives change of water depth with distance along channel
Note
  So and Sf are positive when sloping down in direction of flow
  y is measured from channel bottom
  dy/dx =0 means water depth is _______
yn is when
constant

## Slide 49: Surface Profiles
Mild slope (yn>yc)
  in a long channel subcritical flow will occur
Steep slope (yn<yc)
  in a long channel supercritical flow will occur
Critical slope (yn=yc)
  in a long channel unstable flow will occur
Horizontal slope (So=0)
  yn undefined
Adverse slope (So<0)
  yn undefined
Note: These slopes are f(Q)!

## Slide 50: Surface Profiles
Normal depth
Steep slope (S2)
Hydraulic Jump
Sluice gate
Steep slope
Obstruction
S0 - Sf 1 - Fr2 dy/dx
+ + +
- + -
- - +
Chart: E
yn
yc
yn
yn
Negative if depth less than yn

## Slide 51: More Surface Profiles
S0 - Sf 1 - Fr2 dy/dx
1 + + +
2 + - -
3 - - +
Chart: E
yn
yc
yn
yn

## Slide 52: Direct Step Method
energy equation
solve for Dx
rectangular channel
prismatic channel
Given known section 1 and new depth (y2), find distance to section 2
What is Sf?

## Slide 53
Start at upstream end. Try

## Slide 56: Direct Step Method Friction Slope
Manning
Darcy-Weisbach
SI units
English units
Any other options for Sf?
Chezy!

## Slide 57: Direct Step
prismatic
Limitation: channel must be _________ (channel geometry is independent of x so that velocity is a function of depth only and not a function of x)
Method
  identify type of profile (determines whether Dy is + or -)
  choose Dy and thus yi+1
  calculate hydraulic radius and velocity at yi and yi+1
  calculate friction slope given yi and yi+1
  calculate average friction slope
  calculate Dx

## Slide 58: Direct Step Method
=(G16-G15)/((F15+F16)/2-So)
A
B
C
D
E
F
G
H
I
J
K
L
M
y
A
P
Rh
V
Sf
E
Dx
x
T
Fr
bottom
surface
0.900
1.799
4.223
0.426
0.139
0.00004
0.901
0
3.799
0.065
0.000
0.900
0.870
1.687
4.089
0.412
0.148
0.00005
0.871
0.498
0.5
3.679
0.070
0.030
0.900
=y*b+y^2*z
=2*y*(1+z^2)^0.5 +b
=A/P
=Q/A
=(n*V)^2/Rh^(4/3)
=y+(V^2)/(2*g)

## Slide 59: Standard Step
Given a depth at one location, determine the depth at a second given location
Step size (x) must be small enough so that changes in water depth aren’t very large. Otherwise estimates of the friction slope and the velocity head are inaccurate
Can solve in upstream or downstream direction
  Usually solved upstream for subcritical
  Usually solved downstream for supercritical
Find a depth that satisfies the energy equation

## Slide 60: What curves are available? Steep Slope
Chart: distance upstream (m)
| 0 | 0.59739135856291958 | 1.1943072519673501 | 1.7906393548672981 | 2.3862492868425287 | 2.9809586361933338 | 3.5745350691104192 | 4.1666727216442689 | 4.7569641011848134 | 5.3448591419710478 | 5.9296044132837924 | 6.5101509220828806 | 7.0850108298854346 | 7.6520283286278259 | 8.2080005418740019 | 8.7480235415479104 | 9.2643030923554672 | 9.7438374531777381 | 10.163455227777941 | 10.477634504438353 | 10.581490173209316 | 10.145823553014099 | 6.5691365110535855 | 11.084748461023342 | 13.355561482700558 | 15.111759851154709 | 16.580124387562559 | 17.754958490930296 | 18.45067373410641
bottom | 0 | 0.02987 | 0.059715 | 0.089532 | 0.11931 | 0.14905 | 0.17873 | 0.20833 | 0.23785 | 0.26724 | 0.29648 | 0.32551 | 0.35425 | 0.3826 | 0.4104 | 0.4374 | 0.46322 | 0.48719 | 0.50817 | 0.52388 | 0.52907 | 0.50729 | 0.32846 | 0.55424 | 0.66778 | 0.75559 | 0.82901 | 0.88775 | 0.92253
surface | 0.866 | 0.86587 | 0.86572 | 0.86553 | 0.86531 | 0.86505 | 0.86473 | 0.86433 | 0.86385 | 0.86324 | 0.86248 | 0.86151 | 0.86025 | 0.8586 | 0.8564 | 0.8534 | 0.84922 | 0.84319 | 0.83417 | 0.81988 | 0.79507 | 0.74329 | 0.53446 | 0.73024 | 0.81378 | 0.87159 | 0.91501 | 0.94375 | 0.94853
yc | 0.27145 | 0.30131 | 0.33116 | 0.36098 | 0.39076 | 0.42049 | 0.45017 | 0.47978 | 0.50929 | 0.53869 | 0.56793 | 0.59695 | 0.6257 | 0.65405 | 0.68185 | 0.70885 | 0.73466 | 0.75864 | 0.77962 | 0.79533 | 0.80052 | 0.77874 | 0.5999 | 0.82568 | 0.93922 | 1.027 | 1.1005 | 1.1592 | 1.194
yn | 0.20506 | 0.23493 | 0.26477 | 0.29459 | 0.32437 | 0.3541 | 0.38378 | 0.41339 | 0.4429 | 0.4723 | 0.50154 | 0.53056 | 0.55931 | 0.58766 | 0.61546 | 0.64246 | 0.66827 | 0.69225 | 0.71323 | 0.72894 | 0.73413 | 0.71235 | 0.53351 | 0.75929 | 0.87283 | 0.96064 | 1.0341 | 1.0928 | 1.1276
S1
S3
Is there a curve between yc and yn that increases in depth in the downstream direction? ______
NO!
yn

## Slide 61: Mild Slope
Chart: distance upstream (m)
| 0 | 3.334061123644231 | 6.8185716551969469 | 10.512968650525519 | 14.515459904344587 | 19.005167095578024 | 24.362739400249744 | 31.648822288124119 | 46.574001500328315 | 20.41594311348009 | 15.618588710863682 | 13.696454478536564 | 12.892611694705574 | 12.670671643037167 | 12.796218130354541 | 13.145564119600934 | 13.64524160061838 | 14.247885470241068 | 14.921066036034158 | 15.641534115216457 | 16.392003089030773 | 17.159224545661132 | 17.932764742083577 | 18.704174488034607 | 19.466378327059633 | 20.213170808346259 | 20.938728296811348 | 21.637027710165068 | 22.300982449333951
bottom | 0 | 0.01667 | 0.034093 | 0.052565 | 0.072577 | 0.095026 | 0.12181 | 0.15824 | 0.23287 | 0.10208 | 0.078093 | 0.068482 | 0.064463 | 0.063353 | 0.063981 | 0.065728 | 0.068226 | 0.071239 | 0.074605 | 0.078208 | 0.08196 | 0.085796 | 0.089664 | 0.093521 | 0.097332 | 0.10107 | 0.10469 | 0.10819 | 0.1115
surface | 0.45 | 0.45303 | 0.45682 | 0.46166 | 0.46803 | 0.47684 | 0.49 | 0.51279 | 0.57378 | 0.42935 | 0.39173 | 0.36848 | 0.35083 | 0.33608 | 0.32307 | 0.31118 | 0.30004 | 0.28942 | 0.27915 | 0.26912 | 0.25923 | 0.24943 | 0.23966 | 0.22988 | 0.22006 | 0.21016 | 0.20015 | 0.19 | 0.17969
yc | 0.27145 | 0.28812 | 0.30554 | 0.32401 | 0.34402 | 0.36647 | 0.39326 | 0.42969 | 0.50432 | 0.37352 | 0.34954 | 0.33993 | 0.33591 | 0.3348 | 0.33543 | 0.33717 | 0.33967 | 0.34268 | 0.34605 | 0.34965 | 0.35341 | 0.35724 | 0.36111 | 0.36497 | 0.36878 | 0.37251 | 0.37614 | 0.37963 | 0.38295
yn | 0.33799 | 0.35466 | 0.37208 | 0.39056 | 0.41057 | 0.43302 | 0.4598 | 0.49623 | 0.57086 | 0.44007 | 0.41608 | 0.40647 | 0.40245 | 0.40134 | 0.40197 | 0.40372 | 0.40622 | 0.40923 | 0.4126 | 0.4162 | 0.41995 | 0.42379 | 0.42765 | 0.43151 | 0.43532 | 0.43906 | 0.44268 | 0.44618 | 0.4495
If the slope is mild, the depth is less than the critical depth, what happens next?
Rapidly varied flow!
When dy/dx is large then V isn’t normal to cs
Hydraulic jump! Check conjugate depths

## Slide 62: Water Surface Profiles: Putting It All Together
2 m
10 cm
S = 0.005
Sluice gate
reservoir
1 km downstream from gate there is a broad crested weir with P = 1 m. Draw the water surface profile.

## Slide 63: Wave Celerity
Fp1
y+y
V+V
V
Vw
unsteady flow
y
y
y+y
V+V-Vw
V-Vw
steady flow
V+V-Vw
V-Vw
Fp2
Per unit width

## Slide 64: Wave Celerity: Momentum Conservation
y
y+y
V+V-Vw
V-Vw
steady flow
Per unit width
Now equate pressure and momentum

## Slide 65: Wave Celerity
Mass conservation
y
y+y
V+V-Vw
V-Vw
steady flow
Momentum

## Slide 66: Wave Propagation
Supercritical flow
  c<V
  waves only propagate downstream
  water doesn’t “know” what is happening downstream
  _________ control
Critical flow
  c=V
Subcritical flow
  c>V
  waves propagate both upstream and downstream
upstream

## Slide 67: Discharge Measurements
Sharp-Crested Weir
V-Notch Weir
Broad-Crested Weir
Sluice Gate
Explain the exponents of H!

## Slide 68: Summary (1)
All the complications of pipe flow plus additional parameter... _________________
Various descriptions of energy loss
  Chezy, Manning, Darcy-Weisbach
Importance of Froude Number
  Fr>1 decrease in E gives increase in y
  Fr<1 decrease in E gives decrease in y
  Fr=1 standing waves (also min E given Q)
free surface location
Chart: E

## Slide 69: Summary (2)
Methods of calculating location of free surface (Gradually varying)
  Direct step (prismatic channel)
  Standard step (iterative)
  Differential equation
Rapidly varying
  Hydraulic jump

## Slide 70: Broad-crested Weir: Solution
0.5
yc
E
Broad-crested
weir
yc=0.3 m

## Slide 71: Summary/Overview
Energy losses
  Dimensional Analysis
  Empirical

## Slide 72: Energy Equation
Specific Energy
Two depths with same energy!
  How do we know which depth is the right one?
  Is the path to the new depth possible?
Chart: E

## Slide 73: What next?
Water surface profiles
  Rapidly varied flow
    A way to move from supercritical to subcritical flow (Hydraulic Jump)
  Gradually varied flow equations
    Surface profiles
    Direct step
    Standard step

## Slide 74: Hydraulic Jump!

## Slide 75: Open Channel Reflections
Why isn’t Froude number important for describing the relationship between channel slope, discharge, and depth for uniform flow?
Under what conditions are the energy and hydraulic grade lines parallel in open channel flow?
Give two examples of how the specific energy could increase in the direction of flow.

## Slide 76: Water Surface Profiles: Putting It All Together
2 m
10 cm
Sluice gate
reservoir
1 km downstream from gate there is a broad crested weir with P = 1 m. Draw the water surface profile.
1
yc
E
yc=? m
yn
M1
M3
yn
Chart: E or M